## Slide 1: Toolbox Physical load
Company name and date
Notes: Instructions
Welcome participants to the Physical Stress Toolbox.
Introduction: Physical stress is a topic that affects us all, whether you work in an office, production, or warehouse. It's essential to understand how we can protect our bodies from strain and injury so we can stay safe and healthy at work. During this toolbox session, we will explore the various aspects of physical stress, including how it affects our bodies, the associated risks, and important preventive measures we can take to avoid injury. We will share practical tips and guidelines that you can immediately apply in your daily work.
Our goal is not only to raise awareness of the dangers of physical stress but also to equip you with the knowledge and tools you need to work safely and healthily. We encourage you to actively participate in the discussion, ask questions, and share your experiences so we can work together to create a safer work environment for everyone.
Thank you for joining us, and let's learn and grow together during this physical stress session!

## Slide 2: Contents
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
What is physical load?
What are the risks of physical load?
What are the guideline values?
What can you do yourself? Areas for improvement!
Need help?
Notes: Instructions
Briefly explain the various components of the program and, if necessary, make arrangements for asking questions or sharing experiences.
The more interactive the session, the greater the participant engagement.

## Slide 3: How can you exert a physical load on your body?
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
1. By lifting something heavy
2. By working in a seated position
3. By working in a crouched position
4. In all of the above ways
Notes: Instructions: Ask participants to consider how the body can be physically stressed. What exactly is physical stress? What do you do?
Answer: D
There are various forms of physical stress, or ways to physically strain your body. Within the Metal Industry, we primarily see the following forms of physical stress (see also the next sheet):
- lifting and carrying
- pushing and pulling
- strenuous work postures
- repetitive movements

## Slide 4: Forms of physical load
Do you contort yourself into awkward positions? I work safely and healthily!
Safe and healthy working practices | Physical load
Lifting and carrying
Pushing and pulling
Stressful working posture
Repetitive movements
Sedentary work
Notes: Definitions:
Lifting: Lifting involves grasping an object with the hand(s) and then moving it vertically without mechanical aids, without the task performer walking.
Carrying: Holding the load while the worker walks.
Pushing and pulling: Exerting force with the hands on an object.
Strengthening work postures: Static load: Static load refers to a state of permanent tension in a muscle (group) without relaxation. This means that blood flow to the muscle is impaired after a certain period of time. Blood flow is necessary to supply oxygen and nutrients. In addition, blood flow removes waste products. Poor blood flow can lead to health problems.
Dynamic load: Dynamic load alternates between muscle tension and relaxation. Unlike static load, this type of load actually improves blood flow. In principle, dynamic load is less likely to cause fatigue. It can therefore be sustained longer than static load. But joints, muscles, and tendons can also become overloaded due to frequent or prolonged heavy (dynamic) loading.
Repetitive movement: A movement with the hands, arms, and/or fingers that is repeated repeatedly (more than twice per minute). Movements are considered repetitive:
When performed for at least 2 hours spread out over the day, or;
When performed continuously for at least 1 hour.
Holding a weight, such as a tool, is considered repetitive if the weight is less than 3 kilos. A heavier weight is considered lifting or carrying.
Sedentary work: Sedentary work is defined as sitting for more than 1 hour per day. For this occupational health and safety catalogue, we limit this section to sedentary work in the office, especially because sedentary work should be encouraged in production environments.

## Slide 5: What are the possible signs of physical load?
Do you contort yourself into awkward positions? I work safely and healthily!
Safe and healthy working practices | Physical load
1. Nagging (back) pain
2. Tendonitis
3. Hernia
4. In all of the above ways
Notes: Instructions: Ask participants to consider how the body can be physically overloaded. These signals are important to recognize as signs of overloading the body.
Answer: D
All examples of complaints are signs of overloading the body.
Physical overload can cause various health problems, ranging from temporary complaints to serious and chronic conditions. Some common illnesses and conditions that can be caused by physical overload include:
- muscle strain
- tendonitis, such as tennis elbow
- bursitis
- carpal tunnel syndrome
- lumbar sprain or herniated disc
- osteoarthritis
It is important to take physical overload seriously and take appropriate measures to prevent injury. At the first signs, it is also important to consult a general practitioner/occupational health physician.

## Slide 6: Physical load: the risks
Is it a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Physical complaints
  Back
  Shoulders
  Neck
  Hips
  Knees
General fatigue
Standing work
  Varicose veins
Sedentary work
  Reduced blood flow
Notes: Instructions:
There are many different risks associated with physical strain, ranging from physical complaints to general fatigue.
The key rule is that after an evening/night's rest, you should be fully recharged for the next (work)day. If you get out of bed feeling tired, you may be overexerted and not recovering sufficiently.
Varicose veins due to standing work: Prolonged standing can slow blood circulation and increase venous pressure, leading to varicose veins. This is often the case for people who have to stand for long periods of time due to their profession.
Reduced blood circulation due to sedentary work: During sedentary work, certain muscles are constantly used to maintain posture, even when there is little movement. This constant activity of certain muscle groups can lead to fatigue and tension in those muscles and reduced blood circulation throughout the body.

## Slide 7: The back
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: TIP! Ask participants if they have experience with back pain and if they'd like to share anything about it (cause, treatment, what they learned, what they're doing differently now).
Instructions
We'll focus on an important part of our body where pain often occurs: the back!
The back consists of the vertebral column, also called the backbone. This complex structure consists of a series of 33 vertebrae, stacked on top of each other and connected by joints, ligaments, and muscles. It serves as the central support structure of our skeleton and protects the spinal cord, which is located in the spinal canal.
The vertebral column is divided into several segments, including:
Cervical spine (neck): Consists of 7 vertebrae (C1 to C7).
Thoracic spine (chest): Consists of 12 vertebrae (T1 to T12).
Lumbar spine (lower back): Consists of 5 vertebrae (L1 to L5).
Sacral spine (sacrum): Consists of 5 fused vertebrae (S1 to S5).
Coccygeal spine (tailbone): Consists of 3 to 5 fused vertebrae.
Our back (or spinal column) isn't actually straight, but rather has an S-shape (see side view). This ensures the vertebrae are optimally stacked on top of each other, preventing pressure on the intervertebral discs.
If we prevent this natural curvature, additional pressure is placed on the intervertebral discs, and prolonged pressure can cause them to break, and the soft interior can bulge outward.

## Slide 8: Is physical load always bad?
Do you contort yourself into awkward positions? I work safely and healthily!
Safe and healthy working practices | Physical load
1. Yes, of course
2. No, not at all
3. I actually have no idea
Notes: Instructions: Ask participants whether physical strain is inherently bad for the body.
Answer: 2
Physical strain itself is necessary for proper functioning. Problems arise with OVERload or UNDERload.
If we don't strain our bodies, we don't function well. Consider, for example, an astronaut; they don't strain a large part of their body in space. Due to weightlessness, bones, for example, are unnecessary. In the weightless environment of space, our bones don't experience the normal mechanical stress they would on Earth. This leads to a decrease in bone density and an accelerated loss of bone mass, known as space-related osteoporosis or bone resorption. In other words, we need some form of physical strain to function properly.

## Slide 9: What causes you to lose your balance?
Do you contort yourself into awkward positions? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Instructions
When you experience complaints, there's an imbalance between workload and capacity.
TIP! Ask participants for examples of how you become unbalanced. Consider using a flipchart or whiteboard with two columns to gather examples of workload and capacity.
For example, ask for examples of workload that is too high (such as work duration, frequency, insufficient rest breaks, the required posture, varying posture, and environmental factors such as temperature or workstation layout).
Also ask for examples of workload (such as good physical condition, a healthy lifestyle, not overdoing it, avoiding stressors, using good work techniques).
Workload
What you have to deal with
Capacity
What you can handle (both physically and mentally)

## Slide 10: Imbalance
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Imbalance arises when you push yourself beyond your limits!
Too much strain
Or
Too little resilience
You become unbalanced when you push yourself beyond your limits! Not everyone is equally strong or fit.
This explains the differences between employees; consider, for example, the differences between young and old. With increasing age, physical resilience (generally) simply decreases. As a result, an older colleague may not be able to perform all physical tasks as quickly or as strenuously as a younger colleague. This difference also exists between men and women. Women (generally) simply have a lower physical resilience than men. Of course, there are exceptions...
It's important to take these differences and also the decrease in resilience into account. When you're young, you think you can handle anything, but will you be able to keep that up until you're 67? Take the right measures now to avoid being worn out later.

## Slide 11: Lifting
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Instructions
In the next section, we'll delve deeper into several stressful activities, including lifting, pushing and pulling, and stressful work postures.
Lifting involves grasping an object with the hand(s) and then moving it vertically without mechanical aids, without the task performer walking. In metalworking and electrical engineering, employees regularly lift while performing their work. Examples of lifting situations include loading and unloading products from machines, assembly, and changing tools on machines.

## Slide 12: What is the maximum weight you may lift?
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
A. 18 kg
B. 25 kg
C. There is no maximum, whatever you can handle
Notes: Instructions
Employees in metalworking and electrical engineering regularly lift items while performing their work. Examples of lifting situations include loading and unloading products from machines, assembly, and changing tools on machines.
Lifting Guidelines
The maximum lifting weight is 25 kg, depending on the frequency and height.
Objects heavier than 25 kg may only be lifted with assistive devices or by multiple people, with the maximum load per person not exceeding 25 kg.

## Slide 13: Spot the differences
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: In the photos, you see two employees grinding blades. What do you notice about their postures?
Both employees rest their arms on their laps. After all, an arm is a heavy part of the body (5 to 6% of total body weight), requiring us to lift the weight of the blade. The result: the employee bends forward, resulting in:
The employee on the left has a perfectly straight back and is clearly bending from the pelvis.
The employee on the right has a completely bent back in a C-shape.
In both cases, we see significant strain on the neck.

## Slide 14: What is the best lifting technique?
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
A. Back technique
B. Bend your knees
C. Weightlifting technique
D. All of the above
Notes: Instructions: Ask the participants what technique they can use if you lift regularly. And...which technique do they use in practice?
Answer: C
Proper lifting technique prevents damage to the intervertebral discs. The MORE CONVEXED the back, the greater the risk of damage when lifting. So: lift with your back in a hollow/neutral position!
A: Lifting with an arched back is never a good idea. This takes our spinal column out of its natural S-shape and places a lot of force on the intervertebral discs.
B: Fully bending your knees used to be taught as a technique, but it's outdated. It puts too much strain on the knees and is often impractical.
C: With the weightlifting technique (also known as the squat technique), you keep your back straight, but you tilt from the pelvis. So, push your buttocks back. This requires good abdominal and leg muscles. So, TRAIN!
TIP! Ask anyone who goes to the gym. The squat technique is very well-known there. Consider watching a YouTube video of a weightlifter lifting a heavy weight. How does he do this successfully? Pay attention to the position of his feet, the movement of his pelvis, and the moment of inhalation.

## Slide 15: Lifting tips
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
1. Do not lift if you do not have to
2. Keep the load as close to your body as possible
3. Never lift with a twisted back
4. Pick up or put down loads between hip and chest height
Notes: Instructions:
1. It might seem obvious, but don't lift if you don't have to. Use a lifting aid rather than straining your body. Or ask for help.
2. Keep the object as close to your body as possible while lifting. This reduces strain on your back muscles and makes it easier to control the object.
3. Avoid twisting your torso while lifting, as this can place additional strain on your back. Instead, rotate your entire body to maneuver.
4. Lifting at hip and chest height ensures optimal posture. It allows the lifter to keep their back straight and bend their knees, reducing strain on their back and minimizing the risk of injury.

## Slide 16: Guidelines for lifting.
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Maximum 25 kg
Lower weight in case of:
frequent lifting
below knee height
NOT above shoulder height
Notes: Instructions
Guidelines from the Occupational Health and Safety Catalogue:
Lifting between 40-180 cm
Lifting above 1.80 m is undesirable
LIFT FREQUENCY MAXIMUM LIFT WEIGHT in kg
≤ 1x per 10 min 25 kg
> 1x per 10 min - ≤ 2x per min 12.5 kg
> 2x per min - ≤ 4x per min 11.5 kg
> 4x per min - ≤ 6x per min 9 kg
> 6x per min - ≤ 8x per min 7 kg
> 8x per min - ≤ 13x per min 4 kg
Lifting below 40 cm
LIFT FREQUENCY MAXIMUM LIFT WEIGHT in kg
≤ 1x per 20 min 25 kg
> 1 x per 20 min - ≤ 1 x per min 12.5 kg
> 1 x per min - ≤ 2 x per min 11.5 kg
> 2 x per min - ≤ 3 x per min 9 kg
> 3 x per min - ≤ 4 x per min 7 kg
> 4 x per min - ≤ 6 x per min 4 kg

## Slide 17: Which is harder on your back?
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
A. Pulling
B. Pushing
C. Pulling and pushing are equally bad.
Notes: Instructions
Pushing and pulling at work is common and is increasingly replacing lifting loads. Pushing and pulling occurs, for example, when moving carts and rolling containers.
Answer: A
Pushing a cart is generally considered more ergonomic and safer than pulling one. Here are some reasons why pushing a cart is usually preferred:
Better posture: When pushing a cart, the back generally remains straighter than when pulling. This helps maintain the natural curvature of the spine and reduces stress on the back muscles and intervertebral discs.
Less stress on joints: Pushing uses the stronger muscle groups in the legs, such as the quadriceps and glutes, instead of the back and shoulder muscles that are used when pulling. This reduces stress on the joints of the back, shoulders, and neck.
Better stability: Pushing a cart generally provides more control and stability because the weight of the cart is behind the person. This reduces the risk of tipping or slipping, especially on uneven terrain.
Improved visibility: Pushing the cart gives the person a better view of the route ahead, making it easier to avoid obstacles and reducing the risk of accidents.
Easier to stop the cart: When pushing the cart, the person can stop more easily by simply reducing the pushing force or holding the cart steady with their body. Pulling a cart can be more difficult to stop, especially if its weight has built up momentum.

## Slide 18: Pushing and pulling
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: When pushing and pulling, a distinction is made between pushing or pulling with only the hands or legs and applying force with the whole body (for example when moving a wheelie bin).

## Slide 19: Which is harder on your back?
What load are you carrying? I work safely and healthily!
Safe and healthy working practices | Physical load
A. Quickly getting a trolley moving is harder.
B. Slowly getting a trolley moving is harder.
C. It makes no difference.
Notes: Instructions
Would it make a difference to your body to get something moving quickly or slowly?
Answer: A
The starting force required to get a cart moving in one go can easily be twice as high as when the same cart is set in motion slowly.
Getting a cart moving slowly distributes the force evenly over a longer period, which reduces the strain on the body. Rapidly accelerating the cart can lead to excessive strain on muscles and joints, especially in the back and arms.

## Slide 20: Guidelines for pushing and pulling
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Moving loads up to 50 metres: no more than 30 kg pulling force.
Moving loads over 50 metres: no more than 15 kg pulling force.
Tips
Pushing is better than pulling.
Start moving loads slowly.
Push with both hands.
Ensure the floor is flat and free of obstacles.
Notes: Instructions
Pushing and pulling guidelines from the Occupational Health and Safety Catalogue:
The guideline for pushing and pulling is 300 N (30 kg). Activities exceeding the 300 N guideline may only be performed with assistive devices or by multiple people.
Frequency of work per day Maximum force exerted
< 4 x per hour 30 kg/300 N
4-8 x per hour 25 kg/250 N
8-16 x per hour 20 kg/200 N

## Slide 21: Stressful working posture
It is a weighty problem? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Stressful working postures are common in metalworking and electrical engineering. Static postures, for example, occur during welding or activities that require prolonged standing in the same place, such as at a lathe, workbench, or during welding. Dynamic strain can occur during activities such as picking up materials combined with lifting.

## Slide 22: In which position is the load on the body heaviest?
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
A. Sitting
B. Lying down
C. Standing
Notes: Instructions
We'll look at the highest pressure on the intervertebral discs. What do the participants think? Would this be 0 when lying down, for example?
Answer: A
This might come as a surprise, but when we're sitting, we have the highest pressure on our intervertebral discs. See the next slide for more information.

## Slide 23: Postures that put pressure on the intervertebral discs.
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Instructions
This table shows various postures with pressure (in Newtons) on the intervertebral discs.
This may come as a surprise, but when we're sitting, we have the highest pressure on our intervertebral discs. This is especially true if we're also holding a weight and bending forward.
Think back to the posture of the men in "spot the differences"!
Tip!: Ask the participants why the pressure is never 0, even when lying in bed.
Gravity exerts continuous pressure on our intervertebral discs. Therefore, it's never 0 (except in space).
When we lie on our side, the pressure is slightly higher than when we lie on our back. It's even higher when standing, and it's highest when sitting.
Tip!: Ask why the pressure is higher when sitting than when standing.
This is because in a sitting position, our spine is never ideally shaped into an S-shape, which increases the pressure.

## Slide 24: Guidelines for unfavourable working posture
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Working posture to avoid
  Neck : do not bend or turn too far forward
  Shoulders : do not hold your arms in front of your body or above shoulder height
  Back : do not bend or turn your back too far forward
  Legs : avoid bent knees and do not squat or kneel
Prolonged standing: stand for a maximum of 4 hours
Notes: Instructions
Achieving work postures and movements should be avoided as much as possible.
A body part should be placed in an extreme position as little as possible.
General guideline: a body part should not be placed in an extreme position for more than two hours total during a workday.

## Slide 25: Repetitive movements
Do you set your limits in time? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Repetitive movements involve repeated movements (in space) of the hands (in cycles) where extreme wrist position is an aggravating factor.
This also includes frequently performing movements of the torso (twisting and bending) and of the legs (kneeling and crouching).
In metalworking and electrical engineering, repetitive movements occur, for example, in assembly-line-like activities and product assembly.
Definition:
A movement of the hands, arms, and/or fingers that is repeated repeatedly (more than twice per minute). Movements are considered repetitive:
When performed for at least 2 hours spread out over the day, or;
When performed continuously for at least 1 hour.
Note: Holding a weight, such as a tool, is considered repetitive if the weight is less than 3 kilos. A heavier weight is considered lifting or carrying.

## Slide 26: Guidelines for repetitive movements
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Avoid repetitive movements as much as possible.
Perform similar movements for a maximum of 2 hours per day or 2 hours consecutively.

## Slide 27: Sedentary work
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Notes: Sedentary work is defined as sitting for more than one hour per day. For this occupational health and safety catalogue, we limit this section to sedentary work in the office, primarily because sedentary work should be encouraged in production environments.
Sedentary work may seem like light work, but prolonged periods in the same position can lead to health problems. This can include lower back, neck, and/or shoulder complaints. Nevertheless, sedentary work is preferable to standing work. Only when significant forces are exerted, large objects are handled, or long distances are required is it preferable to set up a standing workstation.
In metalworking and electrical engineering, sedentary work occurs in office-based activities such as screen work.

## Slide 28: Guidelines for sedentary work
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
There are no specific guidelines, but try to avoid sitting (still) as much as possible:
Be considerate and don’t only get coffee for yourself.
Walk to the printer yourself.
Stand up when making a phone call.
Discuss matters while walking.
Take the stairs instead of the lift.
Walk to a colleague instead of calling or emailing them.
Turn your lunch break into an opportunity to exercise (lunch walk).
Cycle to work.
Install a pedometer and aim for at least 5,000 steps per working day.
Notes: Instructions
There is no international legislation or guideline yet to limit sedentary behavior, as research is still in its infancy. Dutch law also lacks specific guidelines that employers must adhere to. However, sitting is included in a physical activity guideline, which advises avoiding sedentary activities.
No guidelines are included for this component, but the fact sheets provide examples to promote physical activity and perform sedentary work in a healthy way.

## Slide 29: How do we do things at our company?
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
What is your opinion?
Notes: We'll conclude this toolbox with a few statements to help you understand how you handle physical strain.
We'll also look at how we're doing here in our company and what we can do to address it.

## Slide 30
Statement 1
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Before I start work, I think about how I can do the work in a healthy way.
A. True
B. False
Notes: Answer: Both can be good...
It's wise to consider how to perform your work efficiently and how to do it healthily. Sometimes you've been doing something for a long time and don't need to think about it anymore. However, be aware of ingrained patterns that aren't always healthy.

## Slide 31
Statement 2
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
The more heavy work I do,
the less I need to go to the gym.
A. True
B. False
Notes: Answer: Both can be good...
This obviously depends on the type of work you do. Work can provide physical training and fitness, but it's especially helpful to support this with exercise. The stronger your body, the greater your resilience. Work is often one-sided in a certain area. Maybe you lift a lot, but don't do much for your endurance. Or maybe you're in an office, in which case you need to move more.

## Slide 32
Statement 3
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
In my free time, I take good care of myself
so that I stay fit for work.
A. True
B. False
Notes: Answer: (hopefully) A
Think of excessive alcohol consumption, too little sleep, smoking, and drug use (lifestyle).

## Slide 33
Statement 4
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Physical overload leads
to back problems.
A. True
B. False
Notes: Answer: True AND false. Physical overload can lead to back pain (most common), but also to muscle, tendon, and ligament problems (soft tissue), and joint problems.

## Slide 34
Statement 5
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
If I have back pain, I just carry on.
A. True
B. False
Notes: Answer: (hopefully) B
It's important to take your body's complaints seriously. So don't act tough, but sound the alarm if your body needs it.

## Slide 35
Statement 6
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Using a lifting aid takes more time.
That's why I don't use it.
A. True
B. False
Notes: Answer: False
It's important to note that the effectiveness of using lifting aids depends on several factors, including the nature of the work, the availability and accessibility of lifting aids, the training and skill of personnel, and the specific circumstances of each situation. In some cases, manual lifting may be faster, but this often comes at the expense of the long-term health and safety of workers.

## Slide 36
Statement 7
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
My age has no influence on
what I can do physically.
A. True
B. False
Notes: Answer:
False. Age definitely affects a person's physical resilience.

## Slide 37
Statement 8
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Bending your knees is
an outdated lifting technique.
A. True
B. False
Notes: Answer:
True. This technique is too taxing on the knees and often impractical. It's better to choose the weightlifting technique.

## Slide 38
Statement 9
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
In terms of the strain on your back, it makes no difference
whether you push a truck with one or two hands.
A. True
B. False
Notes: Answer:
False. Two hands create more symmetry, resulting in a straighter back.

## Slide 39
Statement 10
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Pushing is harder on your back than pulling.
A. True
B. False
Notes: Answer:
False; pulling places more shear forces on the lower back.

## Slide 40
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
The results of the Physical Load Improvement Check:
Notes: Instructions
Add the results of the completed improvement check here.
We'll delve deeper into this in the next section.

## Slide 41
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
Technical : Tools
Organisational : Rotation and design
Behaviour : Strain and load capacity
What can you do?
Notes: Instructions
Ask participants what challenges they face at work, what they dread, and what they consider difficult.
Have them write down a top three for themselves. Then we'll brainstorm solutions.

## Slide 42
Are you getting fed up? I work safely and healthily!
Safe and healthy working practices | Physical load
What can you do yourself? 10 tips!
1. Lifting should be avoided.
2. Consider the weight you are lifting beforehand.
3. Move products as little as possible on foot.
4. Ensure sufficient variety in your work.
5. Use aids.
6. Keep your back as straight as possible.
7. Ensure that materials are stored at grasping height rather than on the floor.
8. Discuss physical load with each other.
9. Work together to find suitable solutions.
10. Ensure you get sufficient rest and take your body's signals seriously.
Take the Physical Load Improvement Check at www.5xbeter.nl!
Notes: Instructions
To solve physical stress problems, we can think of different categories. Sometimes it's not possible to solve the problem technically, but you can devise organizational or behavioral solutions to manage the risk.
Technical: Use of resources
Organizational: Rotation and organization
Behavioral: Stress/resilience  take care of yourself; listen to your body.

## Slide 43
info@5xbeter.nl | www.5xbeter.nl
Safe and healthy working practices | Hazardous substances
Questions?
Notes: Instructions
Finally, here are some tips for managing your physical stress.
Thank the participants for their (active) participation and, if necessary, make arrangements for the next steps.

## Slide 44
info@5xbeter.nl | www.5xbeter.nl
Safe and healthy working practices | Physical load
Need help?
Discuss it with your manager or contact the health and safety officer.
Consult an Improvement Coach from 5xbeter: www.5xbeter.nl
Or call the FREE Improvement Line: 0800 – 55 55 005