## Slide 1: Toolbox Machine safety: Metal saw
Company name and date

## Slide 2: Contents
Safe and healthy working practices | Machine safety: Metal saw
Why machine safety?
Top 3 accidents
Safe machine
What can you do yourself?

## Slide 3
Source: Work Accident Monitor 2023 – Dutch Labour Inspectorate
Why machine safety?
Large proportion of the number of reported occupational accidents.
Contact with work equipment or object 26%.
Safe and healthy working practices | Machine safety: Metal saw
Accident investigations completed in 2023, broken down by accident type.
Notes: https://www.nlarbeidsinspectie.nl/publicaties/rapporten/2024/08/26/monitor-arbeidsongevallen-2023
The accident type "Contact with work equipment or object" is common in the Industrial sector (42% of accidents in that sector). The majority of accidents involve accidents in which the victim came into contact with moving parts of a machine (69%).

## Slide 4: Guard missing.
Guard missing, but insufficiently effective.
Guard removed.
Incorrect operation.
Safe and healthy working practices | Machine safety: Metal saw
Why machine safety?
Cause of contact with moving parts:

## Slide 5: Clothing/hair/jewellery and gloves get caught in rotating parts.
Serious and permanent injury:
Amputation and fractures of fingers, hands, arms or internal injuries. Fractures and large cuts to other parts of the body resulting in loss of function.
Safe and healthy working practices | Machine safety: Metal saw
Cause of accidents involving metal saws
Failure to clamp the product securely.

## Slide 6: Check that the machine is stable.
Check that the saw blade is shielded.
Safe and healthy working practices | Machine safety: Metal saw
Safe machine
Check that the clamping mechanism is working.
Check whether the power cables, plugs and connections are undamaged.
Check that the emergency stop is readily accessible during use.
Check that measures have been taken to prevent flying chips and liquid.

## Slide 7
What can you do yourself?
Prevent clothing, jewellery and hair from being caught in the sawing machine.
Safe and healthy working practices | Machine safety: Metal saw
Test the emergency stop.
Wear hearing protection at noise levels of 80 dB and above.
Ensure the stability of the machine and the workpiece by using roller conveyors or roller stands, for example.
Never bypass the safety devices.
Do not start work if you have any doubts about the safety of the machine; discuss this with your manager.
If safety devices are missing or have been bypassed, discuss this with your manager.
It is recommended to wear safety goggles.

## Slide 8
info@5xbeter.nl | www.5xbeter.nl
Questions?
Safe and healthy working practices | Machine safety: Metal saw

## Slide 9
info@5xbeter.nl | www.5xbeter.nl
Need help?
Discuss it with your manager or contact the health and safety officer.
Consult an Improvement Coach from 5xbeter: www.5xbeter.nl
Or call the FREE Improvement Line: 0800 – 55 55 005
Safe and healthy working practices | Machine safety: Metal saw